# Functional Test
## Hardware uart test
### Method
Run the Hardware Uart test from the github repository
### Results
Sketch runs and passes data
Switch label is correct.
## Software uart test
### Method
Run the Software UART test from the github repository
### Results
Sketch runs and passes data.
Switch label is correct.
## Low power configuration
### Method
1. M ake the jumper configuration as shown.
2. Attach to computer USB port.
1. Replace the XBee with a series of loads 0mA to 500mA
2. Measure VIN on the Teensy, regulated 3.3v rail, and current load applied
### Results
The internal regulator starts cutting out above 200mA and the voltage quickly drops. Damage not apparent.

## High power configuration
### Method
1. M ake the jumper configuration as shown.
2. Attack to 3.3v stable regulated supply.
3. Replace the XBee with a series of loads 0mA to 500mA
4. Measure VIN on the Teensy, regulated 3.3v rail, and current load applied
### Results
The connection is direct, so the slight current/voltage relationship is due to the source and wire impedance. Notice that at this level, there is no 5v rail.

## LED colors and operations
### Method
1. Run the HW UART code. This will test will test DIO5, DOUT and DIN. Send data from the USB dongle to the Teensy via airwaves to test the signal strength LED.
2. Do the colors match other XBee products?
Function	Arduino shield	USB dongle
RSSI	Green	Green
Air to MCU	"DOUT", Red	"TX", Red
MCU to Air	"DIN", Green	"RX", Green
DIO5	Green	Not Present
PWR	Red	Red

Are you blinded by the lights?
### Results

Function	Silk/Color	Correct?	Brightness OK?
RSSI	Green	Yes	Yes
Air to Teensy	"DIN", Red	Color correct, lable not	Yes
Teensy to Air	"DOUT", Green	Color correct, lable not	Yes
DIO5	Green	Yes	Yes
PWR	Red	Yes	Yes

## Action items/Corrections
1. Twist power LEDs to match other LEDs.
2. Mark PWR to LED and jumper pads.
3. Swap DIN and DOUT lables.